## Slide 1: CPSC 240 Computer Organization and Assembly Language
First Program
Hello World
Instructor: Yitsen Ku, Ph.D.
Department of Electrical Engineering,
California State University, Fullerton, USA

## Slide 2: Open Ubuntu Tuffix on VCL

## Slide 3: a. Search "Virtual" in Portal, and click "Virtual Computing Lab".

## Slide 4: b. Click "Proceed to Login" in the Virtual Computing Lab.

## Slide 5: c. Select "Reservations" in the Virtual Computing Lab.

## Slide 6: d. Click "New Reservation" button to open New Reservation dialog.

## Slide 7: e. Select "ECS Ubuntu 2004 4x10 Tuffix 2020" and select "Duration=1/2/4 hours". Click "Create Reservation" button.

## Slide 8: f. Click "Connect!" to open "Connect" dialog.

## Slide 9: g. Click "Get RDP file" button, and then Click the " ECS Ubuntu 2004 4x10 Tuffix 2020.rdp" file to log in.

## Slide 10: h. Click the "Connect" button to continue.

## Slide 11: i. Click the "Yes" button to continue.

## Slide 12: j. Input password and click the "OK" button to continue.

## Slide 13: Create New Program

## Slide 14: a. Click the "Terminal Emulator" to open the "Terminal Emulator" window.

## Slide 15: b. Input "uname -a" to check the system. The message shows the system is "x86_64 GNU/Linux".

## Slide 16: c. Input the "sudo apt-get install yasm" command to install "yasm" assembler. Input "clear" command to clear the window.

## Slide 17: d. Input "cd Desktop" to change directory to "Desktop". Input "mkdir hello" to create "hello" folder. Input "cd hello" to change directory to "Desktop/hello".

## Slide 18: d. Input "touch hello.asm" to create "hello.asm" file. Input "ls" to show the file in the "hello" folder. Input "gedit hello.asm" to edit "hello.asm" file.

## Slide 19: e. Input the program as follows: Click "Save" button to save the program to "hello.asm". Click "X" to return to "Terminal Emulator".

## Slide 20: f. Input "yasm -g dwarf2 -f elf64 hello.asm -l hello.lst" command to run the assembler and generate "hello.lst" and "hello.o" files. Input "ls" to check the directory.

## Slide 21: g. Input "ld -g -o hello hello.o" command to run the linker and generate "hello" files. Input "ls" to check the "Desktop" directory.

## Slide 22: h. Input "./hello" command to execute the "hello" file and display the execution result of "hello, World!".

## Slide 23: i. Input "nano hello.lst" command to open "hello.lst" file.

## Slide 24: j. The GNU nano will display the "hello.lst" file. Click "X" to return to "Terminal Emulator".

## Slide 25: k. Input "exit" to close the "Terminal Emulator" and return to the "Desktop".

## Slide 26: Upload Program

## Slide 27: a. Switch to "Desktop" and click on "Web Browser" to open "Web Browser".

## Slide 28: b. Open "CSUF portal" and click on the "DropBox"

## Slide 29: c. Click the "Upload/folder" on the Dropbox page

## Slide 30: d. Select the "hello" folder on the Desktop and click the "Upload" button to continue...

## Slide 31: e. The "hello" folder has been uploaded to Dropbox.

## Slide 32: l. Click the "CWID" and select "Log Out…" to terminate the "Remote Desktop" connection and free up bandwidth for other students to use.

## Slide 33: Thanks